## Slide 1: Abilene Update
Rick Summerhill
Associate Director, Backbone Network Infrastructure, Internet2
CUDI Reunión de Primavera 2003
Ensenada, Baja California, México
3 April 2003
Notes: This is a general overview presentation about Internet2. Internet2 is a consortium, led by US universities, which is recreating the partnership among academia, industry and government that fostered today’s Internet in its infancy.

## Slide 2: ¡Muchas Gracias!
Gracias por la invitaciόn a esta reunion de primavera 2003
Es un gran placer el estar aquí
Desafortunadamente, mi Español no es muy bueno - perdones

## Slide 3: Abilene Partnerships
Cisco Systems
Indiana University
Juniper Networks
Nortel Networks
Qwest Communications
UCAID
ITECs: North Carolina, Ohio

## Slide 4: Outline
Abilene Backbone
Abilene Peering
Gigapops and the Quilt
Abilene Challenges
Future Trends in Networking

## Slide 5: Abilene Backbone
IP-over-DWDM (OC-192c) and IP-over-SONET OC-48c Backbone
50 direct connections (OC-3c  10 GigE)
  2 10 GigE connection
  6 OC-48c
  1 GigE connection
  24 connections at OC-12c or higher
  Number of ATM connectors soon down to 6 – discouraging connections
221 participants – research universities & labs
  All 50 states, District of Columbia, & Puerto Rico
Expanded access
  70 sponsored participants
  26 state education networks

## Slide 6
Abilene Backbone - Future

## Slide 7
Abilene Backbone - Current

## Slide 8: Abilene Status - Status
Upgrade in final stages
Atlanta POP is only one not currently installed – approximately a month away
Currently installing OC-192c circuits – all POPs will have OC-192c connections
  Kansas City to Houston
  DC to Atlanta
  Seattle to Sunnyvale
  Seattle to Denver
LA to Houston and Houston to Atlanta scheduled for this summer
Upgrade has gone very smoothly – Kudos to the NOC, Qwest, and Juniper

## Slide 9: And a Real One (NYC)

## Slide 11: Abilene Peering - International (March 2003)
STAR TAP/Star Light
APAN/TransPAC†, CA*net, CERN, CERNET/CSTNET/NSFCNET, NAUKAnet, GEMnet, HARNET, KOREN/KREONET2, NORDUnet, SURFnet, SingAREN, TANET2
NYC
GEANT*,
HEANET,
NORDUnet,
SINET,
SURFnet
Pacific Wave
AARNET, APAN/TransPAC†, CA*net, TANET2
SNVA
GEMNET, SingAREN, WIDE(v6)
L.A.
UNINET
AMPATH
ANSP, REUNA2, RNP2, RETINA (REACCIUN-2)
OC12
El Paso (UACJ-UT El Paso)
CUDI
San Diego (CALREN2)
CUDI
09 January 2002
ARNES, ACONET, BELNET, CARNET, CERN, CESnet, CYNET, DFN, EENet, GARR, GRNET, HEANET, IUCC, JANET, LATNET, LITNET, NORDUNET, RENATER, RESTENA, SWITCH, HUNGARNET, GARR-B, POL-34, RCST, RedIRIS, SANET, SURFNET
† WIDE/JGN, IMnet, CERNet/CSTnet,/NSFCNET, KOREN/KREONET2, SingAREN, TANET2, ThaiSARN
Last updated: 17 March 2003
WASH
GEANT

## Slide 12: Abilene Federal/Research Peering (March 2003)
Chicago
ESNet
Star Light
DTF*, NREN
DREN
Pacific Wave
DREN
SNVA
ESNet
NGIX-West DREN, NISN, NREN, USGS
(MIX)
09 January 2002
NGIX/STAR TAP
DREN, ESNet, NISN, vBNS
USGS
WASH
DARPA SuperNet*
NGIX-East
DREN, NISN, USGS, vBNS
Last updated: 17 March 2003
NYC
ESNet
*Limited Research Peering

## Slide 13: Abilene Peering
Peering Methods
  Preferred is through an exchange point: For example, PacWave, Starlight, MANLAN, AMPATH
    MANLAN should be operational mid-April
    Partnership with NYSERNET for collocation and support
    Supports peering with Abilene, but also between other connectors
    LaLan under investigation, with CENIC
  Direct peering to backbone router
  Peering through Gigapops, through tunnels or BGP

## Slide 14: Gigapops and the Quilt
Great Diversity among the connectors
  The Quilt consists of connectors with four or more member institutions – the major gigapops (CUDI is an affiliate of the Quilt)
  Some connectors consist of a single institution
Variety of Technical/Engineering Approaches
  Variety of different connection types – especially behind the connector
  Many are investigating fiber/wave opportunities at this time
Diversity of Political and Economic Systems
  Some are legal non-profit entities
  Some are informal and organized under a university system
  Many have non-Internet2 members as gigapop participants
  Many Provide commodity services for gigapop participants

## Slide 15: Gigapops and the Quilt
Example: The Great Plains Network (Kansas City)
  Has had a diverse technical and political/economic structure over the past four years – constantly evolving
  Connects I2 members and state networks
    Not all connectors transit Abilene
    Expanded hierarchy – backbone, regional, state, campus, department
  Provides commodity services
  Part of the Quilt fabric

## Slide 16: Gigapops – The Quilt
Quilt Participants
CENIC
FRGP
GPN
Indiana Gigapop
Intermountain Gigapop
MAGPI
MAX
Merit
MREN
Net.Work.Virginia
North Carolina
Northern Lights
NOX
NYSERnet
OARnet
ONEnet
Oregon Gigapop
PNWGP
Pittsburgh Gigapop
SOX
Texas Gigapop

## Slide 17: Abilene Network Challenges
Abilene has primarily been a network for experimentation with Applications
Attempt to provide more experimental network activity and provide measurement data on the Abilene IP Network for research community
A few examples
  Abilene Observatory
  Large MTUs
  IPv6

## Slide 18: Abilene Observatory
A program to provide enhanced support for network research on Abilene
Two Components of the Observatory
  Measurements and data collected by NOC and Engineering Team – The Abilene Measurement Infrastructure (AMI)
  Access to Router Nodes for other projects through Collocation

## Slide 19: Abilene Observatory
Measurements taken by NOC and Engineering Teams
  Four Dedicated Measurement PCs located in the Abilene Racks
  Measurements are Local to the Router Nodes
  Data Eventually Moved to a more central site
  Virtual database for researchers
  Data to be correlated – Potential for the data mining projects to study basic network properties
  CDMA Timing Devices Local to Nodes

## Slide 20: Abilene Observatory
Types of Data
  One-way latency, jitter, loss, reachability
  Regular TCP/UDP throughput tests ~ 1 gbps
  Netflow data, both in raw and summary formats (Ohio ITEC)
  SNMP Data (NOC)
  Routing Data, both IS-IS and BGP - Resiliency
  E2E Performance Beacons, Interactive Potential
  Optical Splitter Taps on Some Backbone Links

## Slide 21: Abilene Observatory
Access to network data archive
  Almost all is easily available, web services
  Access to raw netflow data by special arrangement
    Currently 3 research groups are accessing the raw netflow data
  Preliminary Graphical Representation of Data
  Coherent views of the Abilene network
    Summary View
    Detailed View
  Abilene Management Observation Platform
    Publicly available software
    Merit (Quilt) Participation in testing

## Slide 22: Abilene Observatory
Collocation Component
  Space, power, access is limited, and decreases as more groups participate
  Proposals reviewed by Abilene TAC and NRLC
  Strict requirements concerning installation, access, and monitoring
  Initial project is PlanetLab
    http://www.planet-lab.org

## Slide 23: Large MTUs on Abilene
Basic Ideas
  To serve large flows, must support large MTUs
  Fairly easy to support 9K MTUs
    Most new Ethernet NICs support 9K frames
    Backbones and connector networks should support at least 9K frame sizes
  Internet2 recommendation of 9K
  Potential to experiment with large MTUs on Abilene – requires changes to router and host stacks

## Slide 24: IPv6 on Abilene
Abilene IPv6 Backbone
  Started as a tunnel service, evolved to native, dual stack service, prior to upgrade
  Peering and connectivity does not fall under the Abilene CoU
  Tests – 8 Gbps across backbone, IPv6 only and mixed IPv6/IPv4
  Abilene Measurement Infrastructure includes IPv6

## Slide 25: IPv6 on Abilene
Connectors/Peers (CUDI first native IPv6 peer)
  16 native connections
  14 native peers
Internet2 Programs
  Tutorials very successful
  Much easier than Multicast to deploy and debug

## Slide 26: IPv6 on Abilene
Future Deployments
  IPv6 Multicast
  DNS servers for the .edu community
Applications
  Almost all “simple” applications have been ported
  Typical suspects fairly easy to deploy
    Sendmail, Apache, News
    Oregon has organized a v6 news service with v6 transport, v4/v6 access
  Need to have “large” packages ported

## Slide 27: Future Trends in Networking
Emerging requirements may not be met by a high-performance, yet best-effort IP network
  DWDM: 10-Gbps channels now; 40-Gbps soon
  Computational science grids
    Applications with deterministic network requirements
  Infrastructure for basic and applied networking research
  Dedicated “long” waves for special projects
  Wave exchange points
Moment of unprecedented contrarian economics
  Distressed fiber assets available on national scale
    ‘once in a lifetime’ opportunity
  Optronics industry severely impacted by carrier bust
Future Trends in Networking
  However, optical networking alone does not solve the end-to-end performance problem
    Host configuration (Web100)
    Local networking

## Slide 28: Future Trends in Networking
Packet switching (IPv4/v6 routed cloud)
  +: E2E reachability
  +: advanced services (v6, multicast)
  +: measurement visiblility
  +: network management
  -: shared, best effort service
  -: WAN/LAN bandwidth balance
Circuit switching (Optical circuits; IP/Eth frames)
  +: dedicated capacity for specific purposes (e.g., TeraGrid)
  +: customized network focus (experimental vs operational)
  +: lack of contention for bandwidth
  +: CyberInfrastructure view
  -: inefficient - resource utilization and manpower
  -: abandons tremendous scaling power of IP networks

## Slide 29: Future Trends in Networking
Where are we headed?
The is an important period in the history of networking!
Must constantly be aware of future possibilities
If we were to design Abilene today, how would it look?

## Slide 30: Future Trends in Networking
Fiber Initiatives
  National LambdaRail
  USA Waves
  Fiberco
Potential to provide significant resources to the R&E community

## Slide 31: Summary
Abilene Upgrade in final stages
Provide significant research opportunities into a best effort IP network like Abilene
Continually reassess network opportunities and trends for future implementations of R&E networks